## Slide 1: DEFCON: Generating and Detecting Failure-prone Instruction Sequences via Stochastic Search
Ioannis Tsiokanos*, Lev Mukhanov*, Giorgis Georgakoudis†, Dimitrios S. Nikolopoulos‡, and Georgios Karakonstantis*
*Institute of Electronics, Communications and Information Technology, Queen’s University Belfast, UK
†Center for Applied Scientific Computing, Lawrence Livermore National Laboratory, USA
‡Department of Computer Science, Virginia Tech, USA

## Slide 2: Outline
Introduction & Motivation
Proposed approach & Design flow
Case study: application to an FPU
Experimental results
Conclusions

## Slide 3: Challenge: Circuits more Prone to Failures
Static Variations
Dynamic Variations
Wear-out/Aging
Time [y]
failure
failure
Time [s]
Operations under scaled voltage for energy efficiency
  More sensitive to failures
Source: Intel
Threaten System Functionality and Output Quality

## Slide 4: Addressing Timing Failures
Error mitigation schemes that try to strike a balance between protection efficacy and energy based on:
  adaptive voltage/frequency scaling
Impact evaluation of errors on micro-architecture/applications
Frameworks that try to model timing errors based on:
  Statistical models
  Machine learning algorithms
 Errors are not related to the circuits
 Ignore the impact of all the concurrently executed instructions on error rate
Stress code generation for testing the efficacy of developed methods
  Identify in advance worst-case frequency/voltage fluctuations
 Agnostic of the underlying hardware
 Require custom-made infrastructure
error prediction/detection

## Slide 5: Proposed Approach
DEFCON, a fully automated framework that:
Our Contributions:
Analysis of the impact of instruction execution history
on error rate
Integration of a properly formulated genetic algorithm with accurate post layout gatelevel simulation
Introduction of an application vulnerability metric to quantify the application susceptibility to timing failures
Detects vulnerable code regions in applications
Generates failure-prone
instruction sequences
DEtecting Failure-prone InstruCtiOn SequeNces (DEFCON)

## Slide 6: Dynamic Timing Failures in Pipelined Cores
Factors that affect timing errors:
  Delay increase
  Type of instruction
  Input operands
  Instruction execution history [1]
[1] X. Jiao et al., “Clim: A cross-level workload-aware timing error predic- tion model for functional units,” Trans. on Comp., 2018
Window of 2 instruction impacts error rate
Same Window of 2 instructions manifests NO error
Deep instruction execution history impacts failure rate.
How many instructions within a sequence affect the timing error manifestation?

## Slide 7: Role of Instruction Execution History
Intuition: All the concurrently executed instruction affect the error rate
Experiment Setup
- Design under test: FPU - Pipeline dept: 6
- Input: 1M instruction sequences - 15% clock reduction -> 15% variation-induced delay increase
  - windows of increasing number of concurrently executed instructions
ER = Faulty ISQs / # Total ISQs
Error Rate (ER)
Average Relative Error
avgRE
0
0.5
1
avgRE =
27%
88%
All the instructions preceding the currently executed instruction in the pipeline may trigger a timing failure in this instruction
Evaluations of all parameters that affect timing failures:
6 instruction types, two 64 bits input operands, pipeline-depth=6

## Slide 8: DEFCON Workflow
DEFCON: fast and accurate generation and detection of error-prone instruction sequences
  Synthesis Phase: Genetic algorithm that Generates Stressful Instruction Sequences (ISQs)
  Analysis Phase: Estimates application vulnerability to failures
No
Yes
Validation of Synthesis Phase
DEFCON records all ISQs with non-zero relative error
app sequences are splitted into 2 groups: {failure-prone, failure-free}
Compare

## Slide 9: Case study: Application to an FPU
Application to the mor1kx marocchino pipeline double precision FPU based on OpenRISC Instruction Set Architecture
Targeted FPU consists of 6 pipeline stage
Excellent representatives of complex pipelined designs
Floating point operations dominant in various apps
  Considered apps:
    cg, is, mg and bt from NAS Suite,
    hotspot and k-means from Rodinia Suite
Average instruction distribution

## Slide 10: Experimental Results – GA evaluation
Values of Genetic Algorithm (GA) parameters
Run in parallel on 16 cores of an Intel Xeon system
Generations to converge: 120 generations
Time to converge: 20 hours/core
Number of chromosomes in each generation | Mutation Probability | Crossover Probability
40 | 0.6 | 0.9

## Slide 11: Evaluation Results Worst-case Instruction Sequences Generation
Instruction sequence that maximize output relative error
2 clock reduction (CR) levels -> degrees of variation-induced worst-case delay increase
CR1 -> 15% delay increase
CR2 -> 13% delay increase
Ogold: Error free output Osim : Simulation output
CR2
No failures: 5 / 6 apps
DEFCON reveals 98.5% on average higher maxRE
CR1
No failures: 1 / 6 app
maxRE ranges: 0.007% - 100%
DEFCON reveals significant higher or equal maxRE than apps

## Slide 12: Evaluation Results – Application Vulnerability
Hash based search engine that quickly detects error-prone sequences for each program
Code Vulnerability Factor : CVF
  Quantify the vulnerability of each application
Intuition: Applications with high CVF have higher Error-rate
CR1 (15% clock reduction)
Highest CVF: bt, Lowest CVF: k-means
Highest ER: bt, Lowest ER: k-means
Similar correlation for the other apps
CR2 (13% clock reduction)
ER at CR1 much higher than ER at CR2
CVF at CR1 = 18x CVF at CR1
Notes: Intuitively, we suggest that applications with a high CVF are more vulnerable to failures and thus have a higher ER

## Slide 13: DEFCON Detection Accuracy
DEFCON outcomes of inspecting an app:
DEFCON Target: Achieve high TPR
  Avoid FN outcomes
  Tradeoffs between TPR and TNR
TP: correctly detection as faulty
TN: correctly detection as non-faulty
FP: incorrect detection as faulty
FN: incorrect detection as non-faulty
True Positive Rate (TPR)
True Negative Rate (TNR)
Average TPR | Average TNR
99.7% | 82.2%

## Slide 14: Potential Usecases
Generation of stress code
  DEFCON generates micro-architecture aware stress code that maximizes the quality degradation
  Source of variations:
    Process,
    Temperature,
    Voltage droops, etc..
Reduced voltage operations when CVF = 0
  Power/energy efficiency

## Slide 15: Potential Usecases (II)
DEFCON + Dynamic Clock adjustment = Energy savings for every app
Instruction characterization: DEFCON characterizes each instruction as:
LUT: Look-up table that contains the type of each executed instruction to checks for critical instructions in the pipeline at any instant
Main idea:
Design operates constantly at reduced voltage
(nominal Voltage = 1.1V, reduced Voltage = 0.95V)
Dynamically clock stretching in the case of an error-prone instruction sequence
Critical (error-prone)
Off-critical (error-free)
Critical: clock period increases (15% for 0.95V)
Off-critical: nominal clock period
Apps | hotspot | cg | is | K-means | mg | bt
Energy gains (%) | 26.1 | 27.2 | 28.4 | 29.3 | 28.9 | 21.2

## Slide 16: Conclusion
Our contribution:
DEFCON, a fully automate framework for generating and detecting
failure-prone instruction sequences in pipelined cores
We consider for the first time the full pipeline execution history, instruction type and data dependent path excitation.
We formulate a genetic algorithm driven by accurate gate-level simulation to stochastically search for microarchitecture-aware, failure-prone code.
We detect efficiently and accurately error-prone code regions in applications binary.

## Slide 17: Back-up slides

## Slide 18: Role of Instructions Execution History
Factors that affect timing errors in pipelined designs:
  Delay increase
  Type of instruction
  Input operands of instruction
  Instruction execution history
Besides I6, only I5 affects timing failures on I6
Error Rate (ER)
ER = Faulty ISQs / # Total ISQs
Average Relative Error
avgRE
0
0.5
1
avgRE =
27%
88%
X. Jiao et al., “Clim: A cross-level workload-aware timing error predic- tion model for functional units,” Trans. on Comp., 2018
Experiment Setup
Design under test: FPU
Input: 1M instruction sequences
15% clock reduction -> 15% variation-induced delay increase
Pipeline dept: 6
Instruction sequences plays an important role on
timing failure occurrence
Evaluations of all parameters that affect timing failures:
6 instruction types, two 64 bits input operands, pipeline-depth=6
Notes: Pipeline -> Set of instructions that executed concurrently