## Slide 1: Low Power Variation-Aware Cores based on Dynamic Data-Dependent Bitwidth Truncation
Ioannis Tsiokanos, Lev Mukhanov, Georgios Karakonstantis
ECIT Institute, Queen’s University Belfast
This work is partially supported by the European projects
UniServer (grant no. 688540 ) and OPRECOMP (grant no. 732631)

## Slide 2: Outline
Introduction & Motivation
Proposed approach & Design flow
Case study: application to an FPU
Experimental results
Conclusions

## Slide 3: Challenge: Variations in Nanoscale Era
Transistor shrinking has made circuits more prone to static and dynamic variations
  Up-to 50% delay variations
Such delay variations threaten correct functionality and ultimately yield
#of chips
Frequency
Freq1
Freq2
Freqk
< <

## Slide 4: Conventional Variation-Aware Scheme
Designers address variations/failures by:
  Using pessimistic timing/voltage guardbands
    Based on Static Timing Analysis
Large power/performance overheads

## Slide 5: Approximations & Variation-Aware Designs
Approximate Computing
  Exploit error resilient properties of applications by:
      Scaling precision
      Truncating the bitwidth of operands
Reduce computational delay
 Agnostic of the underlying hardware
 Application to simple arithmetic units
 Static approximation of all data
 Unnecessary quality loss
Operand : 01010101010011101010101010111011
Operand after 10 LSBs truncation : 01010101010011101010100000000000

## Slide 6: Proposed Approach
Target:
  Introduce an occasional dynamic bitwidth truncation to avoid timing failures in pipelined designs
Methods:
    Dynamic prediction of the error-prone Long Latency Paths (LLPs)
        Identify instructions and operands that activate LLPs at runtime
    Path Shaping
        Isolate the LLPs to a single pipeline stage
    Operand bitwidth truncation
        Truncating the bit-width only of the few operands that activate the LLPs

## Slide 7: Method (I) – Dynamic Prediction of LLPs
Identify in advance operands that activate the error-prone LLPs
Ripple carry adder example
Most timing critical path (LLP1): Carry propagation from Ci,0 to Co,3
Identify LLPs activation by monitoring Carry propagation at FA0 & FA1:
SLP1
SLP2
F(0,1) =1 Activation of Long Latency Paths (LLPS)
F(0,1) =0 Activation of Short Latency Paths (SLPs)
F(0,1) = (A0B0)(A1B1)

## Slide 8: Method (I) – Dynamic Prediction of LLPs
Identify LLPs activation by monitoring m - n FAs :
  F(n,m) = (AnBn)  (An+1Bn+1)  …  (Am-1Bm-1)  (AmBm)
Tradeoffs in such a circuit:
  Increase the number of (m-n) bits  Decrease the activation probability of LLPs
    Carry propagation of 1 FA =
    Carry propagation of 4 FAs =
  Increase the number of monitored bits  Increase the area/power dissipation
Application of such a unit to pipelined designs is not so straightforward
SLP1
SLP2

## Slide 9: Method (II) – Path Shaping
Performance-centric ASIC flow
  Primary objective: improvement of performance
  The inherently fast paths are allowed to become slow
  Many long paths from every stage are close to target clock period
Timing wall
  Increased probability of failures
  Use of any error prediction/avoidance scheme in many stages
Clock period
There is a need to move away from such a path distribution
Timing Wall

## Slide 10: Method (II) – Path Shaping
Eliminate the timing wall
Enforce a path distribution with gradual slope, where |SLPs| >> |LLPs|
Render the LLPs less probable
Restrict the LLPs to single pipelined stage, accessed by specific instructions

## Slide 11: Method (III) – Operand Truncation
Dynamically setting to 0 only the LSBs of the operands of the specific instruction(s) that activate the LLPs
Addition of two 8 bits operands
A: 00000001 and B: 01111111
00000001
+ 11111111
110000000
Addition of two operands after 4 LSBs truncation
A: 00000000 and B: 01110000
00000000
+ 11110000
11110000
4 LSBs truncation
No truncation
Carry propagation,
Activation of LLPs
No Carry propagation,
Activation of SLPs
Any quality loss can be controlled by selecting the proper number of truncated bits

## Slide 12: Proposed Design & Analysis Flow
Microarchitectural and Code optimizations
Extra optimization step
Introduction of path-group constraints
Make long paths smaller in number
Not allow the tool to make the naturally fast paths slower
A profiling tool for extracting instruction traces and operands as are being executed on real processors
Exploit the dynamic data-dependent path activation
Simulate the design under potential timing variations
Power, quality, error and dynamic power measurements

## Slide 13: Case study: Application to an FPU
Application to the mor1kx marocchino pipeline double precision FPU based on OpenRISC Instruction Set Architecture
Targeted FPU consists of 6 pipeline stage
Excellent representatives of complex pipelined designs
Floating point operations dominant in various apps
  Considered apps:
    K-means, CFD and Heartwall from Rodinia Suite,
    Raytrace from Parsec Suite
Average instruction distribution

## Slide 14: Path distribution of the Re-designed FPU
Original Design
  Timing wall
  LLPs in 4 out of 6 stages
  Increase probability of failures
Proposed design
  Number and probability of LLPs have been reduced
  LLPs restricted only to Stage 4
  Stage 4: mantissa addition

## Slide 15: Long Latency Paths Prediction Unit (LLPPU)
Adoption of a prediction unit for detecting LLPs activation at Stage 4
Low complexity unit:
  F(n,m) = (AnBn)  …  (AmBm)
number of (m-n) bits
activation probability of LLPs (P(L))
(n,m) |  | (27 , 34) | (27 , 33) | (28 , 33) | (28 , 32)
P(L) (%) |  | 0.62 | 1.1 | 2.71 | 4.98

## Slide 16: Evaluation Results
Application profiling
  Use of a profiling tool to extract real floating-point traces
Simulation under potential worst-case delay increase levels
  Different clock period reductions levels (from 0% up-to 11%)
Designs being compared:
  Dynamic 40 LSBs truncation only of the operands that activate LLPs (Prop)
    Original unmodified design (Orig)
    Static 40 LSBs truncation of all the operands (Trunc)
    Guardband based technique

## Slide 17: Evaluation Results – Bit Error Rate
BER : 8% delay increase
Error: simulation output error-free golden output
Original design (Orig)
  BERs: 1.15% - 66.9% in the mantissa and up-to 37.6% in the exponent
Static 40 truncation (Trunc)
  BERs: up-to 32% in the mantissa and 0% - 15% in the exponent
Proposed design (Prop)
  BERs: 0
Increased BERs in the mantissa and the exponent -> quality loss
CFD
Raytrace

## Slide 18: Evaluation Results – Quality loss
Relative Error (RE)
Orig:
  unacceptable quality degradation even under small delay increase
Trunc:
  Considerable, unnecessary quality loss
Prop:
  Minimization of quality loss up-to 8% delay increase (7 orders of magnitude lower RE than Trunc)
Under 11% delay increase all designs incur unacceptable quality loss
CFD
Raytrace

## Slide 19: Area and Power Penalties
Integration of:
  Path shaping technique
  Long Latency Paths Prediction Unit
    Area overhead: 0.34%
    Power overhead: 4.48% on average
Area and Power Overheads

## Slide 20: Comparison with a Guardband based scheme
Guardband based design: up-scale voltage to avoid failures
  Fast corner cell library (1.25V)
Proposed design eliminate failures at lower voltage
  Typical corner cell library (1.1V)
Applications |  | Power Gains in Prop vs Guardbands (%)
K-means |  | 41.73
Heartwall |  | 44.3
Raytrace |  | 38.76
CFD |  | 38.78

## Slide 21: Conclusions
Framework for eliminating timing failures in pipelined cores by:
  Detecting the excitation of the error-prone long latency paths.
  Redesigning the target circuit in a way that isolate the LLPs in a single stage.
  Dynamically truncating the bitwidth only of the operands that activate the isolated LLPs.
Up-to 44.3% power savings at 0.34% area overhead and minimal quality loss